## Slide 1: Ocean Diver Supplementary Training
The Nitrox Workshop

## Slide 2: Aims
Appreciate the benefits of diving on nitrox
Dive safely in open water using nitrox 32 and nitrox 36 for no stop dives
Plan dives using nitrox with BSAC 88 Tables or air computers
Understand potential equipment implications
Understand the methodology for analysing a blended nitrox mix
To enable BSAC Ocean Divers (or similar) to:

## Slide 3: What is nitrox?
A breathing gas usually having more than 21%O2
The gas composition is defined by the nitrogen and oxygen gas fractions
  Nitrox 21 (Air) = 21% oxygen + 79% nitrogen
  Nitrox 32 = 32% oxygen + 68% nitrogen
  Nitrox 36 = 36% oxygen + 64% nitrogen
As the percentage of oxygen in the nitrox mix is increased, consequently the percentage of nitrogen is reduced
32%

## Slide 4: Why nitrox?
Advantages of nitrox – less nitrogen means
  Increased safety factor when used with air table or computer
  Reduced risk of DCI
Disadvantages of nitrox
  Nitrox divers can still suffer DCI
  Certain equipment must be dedicated to the use of nitrox
  Some methods of cylinder filling can expose cylinders to diving grade oxygen
  Oxygen toxicity (explained later)
Notes: Reduced narcosis and oxygen toxicity not a problem for ODs but included for awareness for the future?

## Slide 5: Ocean Diver Qualification
An Ocean Diver is allowed to dive to a maximum depth of 20 metres
Participate only in “No-Stop” dives using Air, Nitrox 32 or Nitrox 36
Plan dives using an air table or air computer
For example, an Ocean diver who has not dived in the past 24 hours is able to dive within the illustrated no-stop dive envelope

## Slide 6: Oxygen Toxicity
Oxygen can be toxic depending upon:
  The operating depth (pressure) of the dive
  Time of exposure at the operating depth
  The fraction of oxygen in the blended mix
Signs
  Visual or auditory disturbances
  Muscular twitching
  Convulsions
Highly unlikely occurrence for Ocean Divers
O2

## Slide 7: Oxygen Toxicity
Resolution
  Abort the dive and return to surface
Prevention
  Each mix has a defined “Maximum Operating Depth” (MOD), which exceeds the Ocean Diver depth limit of 20 metres:
    Nitrox 32% - 35 metres for NO-STOP dives
    Nitrox 36% - 30 metres for NO-STOP dives
  Always analyse the nitrox mix before use
  Always clearly label the cylinder with:
    Oxygen percentage
    MOD
  Do NOT exceed the MOD for the gas mix
    Further considerations need to be understood as the diver progresses through higher levels of training
Notes: Do NOT exceed the MOD for the gas mix – additional consideration for more highly qualified divers. Included for awareness and to make the point that there are further considerations to be taken into account when progressing qualifications.

## Slide 8: BSAC 88 Tables - Planning a No-Stop Dive
Dive to 20 m for 30 minutes
Depth and/or time is ‘in between’ values
  Use next greater depth
  Use next longer time
Surface Code is E

## Slide 9: Planning Two Dives
Example
First Dive
  20 m for 33 min
  Surfacing Code = F

## Slide 10: Surface Interval Table
Surface Interval 3 hours
Second Dive CTC = C

## Slide 11: Planning - dive two
Second Dive
  Table C
  15 metres
  20 min
  Surface Code = F
Good practice to increase oxygen % for the second dive

## Slide 12: Dive Planning - Computers
Dive computers can be used in exactly the same way as for diving using air:
  Plan the dive, dive the plan
  Use of nitrox 32 & nitrox 36 at OD level requires no changes to:
    Use of the dive planning function
    Use of the computer during the dive
    Access to post dive information
Some computers can be programmed for different nitrox mixes:
  At OD level keep set to air
  Other mixes, and their implications, are covered during training for higher qualifications

## Slide 13: The Nitrox Cylinder
Different labels for “Breathing Air” and “Nitrox”
Cylinders used for nitrox usually need to be periodically cleaned & certified

## Slide 14: Nitrox – Practices
Cleaning of equipment
  Oxygen supports combustion
  Materials and greases must be safe with higher oxygen percentages
  Cylinders exposed to oxygen must be cleaned either periodically removing combustible contaminants or if the cylinder is knowingly exposed to a contaminate
  Some regulators do not require cleaning if used with less than Nitrox 40 (confirm with the manufacturer)
Emergency cylinders
  Avoid filling with nitrox unless oxygen cleaned
Notes: Cylinders exposed to diving grade oxygen must be cleaned periodically removing combustible contaminants – periodically is perhaps not quite the right word. There is a requirement for annual cleaning but additional cleaning may be required between times if the cylinder is exposed to a contaminant – e.g. inadequately filtered air.

## Slide 15: Nitrox – Procedures
Percentages must be checked with an oxygen analyser before use
  Follow analyser manufacturer’s guidance
  Supplied gas should not vary more than ±1% from the desired mix
  Diving beyond these conditions requires additional considerations (e.g. MOD adjustment)
  All cylinders should be clearly marked with oxygen percentage and MOD

## Slide 16: Nitrox – Using an analyser
1. Switch on the gas analyser
3. Slowly open the valve - gas gently hissing out
4. Present the analyser to the cylinder valve
2. Calibration, essential before use

## Slide 17: Nitrox – Analysing a mix
5. Take a reading
6. Record the analysis

## Slide 18: Analysing essentials
Calibrate prior to use
Keep flow rate even and as low as possible
Erratic readings point towards analyser failure
Avoid windy conditions
Avoid moisture
At Ocean Diver level your analysis should be within ±1% of target mix
Store analyser away from elevated oxygen levels

## Slide 19: Summary
Nitrox gas composition
Benefits of nitrox
Ocean Diver qualification
  Maximum operating depth of 20 metres
  For NO-STOP dives only
Oxygen toxicity
Dive planning
  BSAC 88 Tables
  Air (21%) only
Equipment
  Cylinders labelled with gas % and MOD
Gas analysis