## Slide 1: Monte Carlo Neutron Transport Part 1: Criticality
Paul N Smith
26 February 2015

## Slide 2
The Monte Carlo method can be thought of as a form of Numerical Experiment. A game (i.e. a stochastic process) is devised for which the expected value is the value of the parameter or function to be estimated.
The Monte Carlo Method is also a way of evaluating integrals, which can be faster than traditional quadrature methods for high dimensional integrals. When applied to radiation transport the Monte Carlo method can be thought of as a way of evaluating the integral form of the Boltzmann transport equation.
Introduction

## Slide 3
Example: Area of Circle - Estimation of π
Circle: x2 +y2 = 1
y = √(1 – x2)
Area of quarter Circle =
Throw pairs of random numbers, uniformly distributed between 0 and 1: (xi, yi) and tally fraction with xi2 + yi2 <1

## Slide 4
Deterministic method of Integration (e.g. Simpson's Rule)
A Stochastic Method of Integration
Monte Carlo Integration

## Slide 5
What is the Monte Carlo Method?
To use the Monte Carlo method to estimate the value of a parameter, K, it is first necessary to devise a stochastic game with numerical outcome, ξ, such that the Expected value of ξ is equal to K:
E(ξ) = K
Let there be NG possible outcomes: with associated probabilities
Then

## Slide 6
Law of Large Numbers
Now play the Monte Carlo game N times and let Ni denote the number of times that outcome ki is obtained where:
The mean of the results obtained is: and set:
So: Law of Large Numbers Hence:
The mean of the results obtained gives an estimate of K.

## Slide 7
How accurate is the Monte Carlo Method?
The variance is given by:
To estimate V need to tally the squares of the values in addition to the values – not much extra work!
An order of magnitude estimate of the error or uncertainty in the estimated value of K is given by: σ = standard deviation = √ variance
Standard Deviation after N trials is:
Thus the rate of convergence of Monte Carlo is N-1/2

## Slide 8
Probable Error
If the Probable Error is εp then it is equally likely that the error with be greater than ε p or less than ε p
Uniform Distribution:
Normal Distribution:

## Slide 9: Distribution of Error
Q - What fraction of the results are expected to lie within one standard deviation of the mean?
  A – 68% for a Normal distribution
  A – 58% for a Uniform distribution
For a Uniform distribution all results lie within √3 (~1.732) standard deviations of the mean.
For a Normal distribution 5% of the results are expected to lie more than 2 standard deviations from the mean and 0.3% are expected to lie more than 3 standard deviations from the mean.
Q - MONK validation test set has almost 1000 cases, so how many results do we expect to be >3σ from the experimental result?
  A – 0 for a Uniform distribution
  A - ~3 for a Normal distribution

## Slide 10
Central Limit Theorem
The sum of a large number of independent, identically distributed random variables is approximately normally distributed!
Play the game a large number of times and the results will be approximately normally distributed.
The restriction to identically distributed variable can be considerably relaxed.

## Slide 11: Normal Distribution
For a normal distribution:
68% of samples lie within one standard deviation of the mean
95% of samples lie within two standard deviations of the mean
99.7% of samples lie within three standard deviations of the mean
It is equi-probable that the deviation from the mean will be greater or less than 0.6745σ = “probable error”

## Slide 12: Criticality - 1
Want to know the neutron multiplication factor, keff
keff = ratio number of neutrons in a generation to that in the previous generation
If keff < 1 the system is sub-critical and the neutron population will die out
If keff = 1 the system is critical and the neutron population is stable – a reactor
If keff > 1 the system is super-critical and the neutron population will grow without limit – a bomb

## Slide 13: Criticality - 2
At the end of a generation have neutrons left to form the start of the next generation
Each of these neutrons suffers one of two possible fates:
  Absorption
  Escape
Some absorptions lead to fission and hence neutron production
On average each fission results in the birth of ν new neutrons
13

## Slide 14: Estimating keff
Follow path of neutron from birth at a fission via scatters to ultimate fate of fission, capture or escape
Use random numbers from specified statistical distributions and cross sections dependent on material composition to choose direction, energy and distance to be travelled to next collision
At next collision use further random numbers and statistical distributions to determine which nuclide it collides with and what type of collision occurs (scatter, capture or fission)
Want to estimate

## Slide 15: Estimating keff – (2)
For a single capture or escape keff = 0
For a single fission keff = ν = number of neutrons per fission
Tally keff and keff2 for each sample to obtain mean and variance
Or release neutrons in many stages and count the number produced, adsorbed and escaped for each stage to gather the necessary statistics

## Slide 16: Thank you!